## Slide 1: FlyMon: Enabling On-the-Fly Task Reconfiguration for Network Measurement
Hao Zheng, Chen Tian, Tong Yang, Huiping Lin, Chang Liu
Zhaochen Zhang, Wanchun Dou, Guihai Chen

## Slide 2: Network Measurement is Important
Management Decisions
(e.g., Routing or ACL Rules, QoS,...)
Packets
Statistics
Events
Network
Data Center Network
Wide Area Network
...
Management
Traffic Engineering
Performance Diagnosis
Security ...
Measurement
Heavy Hitters
Cardinality Jitters
DDoS Victims ...
Many management tasks rely on real-time traffic events/statistics sensed by underlying measurements.

## Slide 3: Diverse Measurement Tasks
Attribute | Measurement Task
Frequency | per-flow size, heavy hitters, flow size distribution, ...
Distinct | DDoS victims, super spreaders flow cardinality, ...
Max | congestion, head of line, maximum inter-arrival time, ...
 | ...
×
＝
Diverse
Measurement Task!
?
  Key : DstIP – Attr: Distinct(SrcIP)
  Key : 5-tuples – Attr: Frequency(1 or pkt_len)
  Heavy Hitters
  DDoS Victims
At a high level, a measurement task composes of a flow key and a flow attribute.
Sketches are popular schemes for measuring flow attributes due to their memory efficiency and accuracy.
Diverse Flow Key
SrcIP/24
SrcIP
SrcIP-DstIP
5-Tuple
···
?

## Slide 4: Diverse Measurement Tasks
×
＝
  Key : DstIP – Attr: Distinct(SrcIP)
  Key : 5-tuples – Attr: Frequency(1 or pkt_len)
  Heavy Hitters
  DDoS Victims
At a high level, a measurement task composes of a flow key and a flow attribute.
Sketches are popular for measuring flow attributes due to their memory efficiency and accuracy.
Frequency
Distinct
Max
Existence
Others
UnivMon
Linear Counting
MRAC
CocoSketch*
BeauCoup*
CountMin
HLL
SuMax
Counter Braids
Elastic
FCM Sketch
BloomFilter
MV Sketch
Diverse Sketches (Part)
Diverse Flow Key
SrcIP/24
SrcIP
SrcIP-DstIP
5-Tuple
···
?
Diverse
Measurement Task!

## Slide 5: Limited Task Capacity in Hardware
Conventional implementation of sketches occupies exclusive hardware resources on programmable switches.
Conventional implementation of a count-min sketch (CMS).
Hash
ADD
index=2
SRAM
SALU
PHV
32-bit
SrcIP
DstIP
Count-min Sketch
A switch accommodates less than 6 sketches in a common case.
Limited Task Capacity. It is impossible to configure all needed tasks in hardware switches.
Fixed Key
Fixed Operation
Fixed Memoy

## Slide 6: Measurement Reconfiguration is Necessary
Tenant | Action
A | ADD Task
B | ADD Task
Tenant | Action
B | ADD Task
Tenant | Action
A | DEL Task
A | ADD Task
Time
Task Capacity = 4
Task Capacity = 4
Task Capacity = 4
t1
t2
t3
Case#1. To cope with changing measurement demands of tenants or applications.

## Slide 7: Measurement Reconfiguration is Necessary
Tenant | Action
A | ADD Task
B | ADD Task
Tenant | Action
B | ADD Task
Tenant | Action
A | DEL Task
A | ADD Task
Time
Task Capacity = 4
Task Capacity = 4
Task Capacity = 4
t1
t2
t3
Measurement Task Reconfiguration can timely and accurately meet the changing measurement demands.
Case#1. To cope with changing measurement demands of tenants or applications.

## Slide 8: Measurement Reconfiguration is Necessary
Operator
Please wait...
We are trying!
Measurement Task Reconfiguration brings more visibility of the network by giving more statistics.
Case#2. To fast locate the root cause of ongoing network anomalies.
User
High drop rate!
High latency!

## Slide 9: State of the Art
Solution#1. Design general or versatile sketches to support multiple measurement tasks simultaneously.
Multi-Attribute Algorithm: UnivMon (SIGCOMM’16), Elastic (SIGCOMM’18), SuMax (NSDI’20),...
Multi-Key Algorithm: BeauCoup(SIGCOMM’20), CocoSketch (SIGCOMM’21).
It’s hard to design a full-key and full-attribute sketch!
Solution#2. Leverage compile-phase programmability of RMT switches to change hardware functions.

## Slide 10: State of the Art
Solution#2. Leverage compile-phase programmability of RMT switches to change hardware functions.
HLL
.p4
Count-Min
d=3
w=32768
HyperLogLog
w=4096
Traffic Interrupt！
It will interrupt running network traffic to reload the data-plane codes.
Solution#1. Design general or versatile sketches to support multiple measurement tasks simultaneously.
Multi-Attribute Algorithm: UnivMon (SIGCOMM’16), Elastic (SIGCOMM’18), SuMax (NSDI’20),...
Multi-Key Algorithm: BeauCoup(SIGCOMM’20), CocoSketch (SIGCOMM’21).

## Slide 11: FlyMon Design
M | A
Key-selection
Attribute-oper.
Runtime
Rules
M | A
M | A
M | A
M | A
M | A
Addr Translation
Runtime
Rules
Basic Idea: dynamically compose a task implementation with Match Action Tables.
On-the-Fly Task Reconfiguration
Dynamic
Attribute(sketch)
Dynamic
Key
Dynamic
Memory
+
+
Hash
Unit
SRAM
PHV
Data Plane
Control Plane
SALU

## Slide 12: FlyMon Design
M | A
Key-selection
Attribute-oper.
Runtime
Rules
M | A
M | A
M | A
M | A
M | A
Addr Translation
Runtime
Rules
Basic Idea: dynamically compose a task implementation with Match Action Tables.
On-the-Fly Task Reconfiguration
Dynamic
Attribute(sketch)
Dynamic
Key
Dynamic
Memory
+
+
Hash
Unit
SRAM
PHV
Data Plane
Control Plane
SALU
Composable Measurement Unit
(CMU)

## Slide 13: Key-selection Phase
Dynamic Key
Candidate Keys
PHV
Hash Unit
SrcIP
DstIP
Select Key
SrcIP
DstIP
IP-Pair
Address
Basic Implementation. Dynamically select an input key (e.g., by masking) for Hash Units through a match-action table.

## Slide 14: Key-selection Phase
Dynamic Key
Candidate Keys
PHV
Hash Unit
SrcIP
DstIP
DstIP
Select Key
SrcIP
DstIP
IP-Pair
PHV Copy
Address
Basic Implementation. Dynamically select an input key (e.g., by masking) for Hash Units through a match-action table.
Challenge: PHV Copy.
It needs to statically allocate extra PHV memory and copy the original header fields to this memory. For example, taking 5-tuple as a key needs additional 104 PHV bits for each SALU.

## Slide 15: Key-selection Phase
Main Optimization: Less-copy Strategy.
Perform one-way compressions (i.e., the fingerprints of candidate keys) with several hash units.
Dynamic Key
Candidate Keys
SrcIP
DstIP
Hash Unit
M1
M2
Hash Unit
Address
Select Key
⊕
PHV
“Compressed” Keys
(e.g., 104 bit to 24-bit fingerprints)
Shared by multiple CMUs

## Slide 16: Key-selection Phase
Main Optimization: Less-copy Strategy.
Perform one-way compressions (i.e., the fingerprints of candidate keys) with several hash units.
One-way Compressions
Decide which keys to hash in the control plane with the dynamic hashing feature of RMT hardware (i.e., Tofino)
1
Dynamic Key
Candidate Keys
SrcIP
DstIP
Hash Unit
M1
M2
Hash Unit
Address
Select Key
⊕
PHV
“Compressed” Keys
(e.g., 104 bit to 24-bit fingerprints)
Shared by multiple CMUs
Notes: Firstly, we generate several compressed keys with hash units.
We can decide which keys to compress in the control plane with the dynamic hashing feature of RMT hardware.

## Slide 17: Key-selection Phase
Select one of the
“Compressed” keys
XOR between keys is supported.
2
Main Optimization: Less-copy Strategy.
Perform one-way compressions (i.e., the fingerprints of candidate keys) with several hash units.
Dynamic Key
Candidate Keys
SrcIP
DstIP
Hash Unit
M1
M2
Hash Unit
Address
Select Key
⊕
“Compressed” Keys
(e.g., 104 bit to 24-bit fingerprints)
Shared by multiple CMUs
PHV
Deploy ~5x CMUs when the candidate key size reaches 360 bits.

## Slide 18: Attribute-operation Phase
Select Operation*
ADD
OR
?
?
ADD
SALU
Operation Capacity = 4
SRAM
UnivMon
Linear Counting
MRAC
CocoSketch*
BeauCoup*
Frequency
Distinct
CountMin
HyperLogLog
SuMax
Counter Braids
Elastic
Max
Existence
FCM Sketch
Bloom Filter
MV Sketch
Others
Various Sketches
Challenge: Limited Stateful Operations.
It is challenging to support various sketching algorithms with the limited SALU operations (e.g., only 4 for each SALU in Tofino).
Address
Basic Implementation. Select a pre-loaded operation through a match-action table.

## Slide 19: Attribute-operation Phase
Main Optimization: A Reduced Operation Set
CMS
MRAC
TowerSketch
Counter Braids
SuMax(Sum)
SuMax(Max)
HyperLogLog
Bloom Filter
Linear Counting
BeauCoup
Frequency
Max
Distinct
Exist.
Generation process of the reduced operation set.
Built-in Algorithms
UnCond-ADD
MAX
AND
OR
Cond-ADD
Decomposition
Cond-ADD
AND-OR
MAX
Reduced
Operation Set
XOR/MIN/...
Reserved Operation
Aggregation
Built-in Algorithms. We only try to support simple but dedicated measurement algorithms to cover common flow attributes.
FlyMon uses 3 stateful actions to implement at least 10 sketches.
(See implementation details in the paper)
Decomposion. Sketches can share some joint operations.
Aggregation. Some operations can be aggregated into a single stateful action.

## Slide 20: Dynamic Memory Management
Challenge: Limited SALUs (i.e., CMUs)
  Coarse-grained memory allocations
  Limited Concurrent Measurement Tasks.
CMU 0
CMU 1
CMU 2
Task 0
Unused
Task 1
Subunit-level Dynamic Memory with Address Translation Mechanism.
Unit-level Dynamic Memory with runtime reconfigurable CMUs.
CMU 0
CMU 1
CMU 2
Task 0
Task 0
T1
T2
T1
Task 3
Task 4
T2

## Slide 21: Dynamic Memory Management
SRAM
Task 2
…
Task 1
TCAM-based Translation
Match |  | Action
Task1 Filter |  | 
Task 2 Filter |  | 
... | ... | ...
Default |  | NoAction
Match |  | Action
Task1 Filter |  | 
Task 2 Filter |  | 
... | ... | ...
Default |  | NoAction
Task 2
addr =
addr =
Address Translation Mechanism: maps a selected key to the memory range of the task to be performed.
  TCAM-based Translation can complete address translation in one MAU stage.
  Shift-based Translation (see details in the paper).

## Slide 22: CMUs in RMT Pipeline
Each CMU has 4 types of stages:
          Compression Stage
          Initialization Stage
C
I
Key-selection
Phase
      Preparation Stage
      Operation Stage
P
O
Attribute-oper.
Phase
Composable Measurement Unit
SALU
SRAM
Address
Translation
Params
Processing
Set
Key
Set
Params
Initialization
Preparation
Operation
…
HASH 1
Compression
M
1
M
2
M
X
HASH 2
HASH
Based on the optimizations, here is a complete view of CMUs in the RMT pipeline.
The logical view of a CMU in RMT pipeline
Address
Translation

## Slide 23: CMUs in RMT Pipeline
Based on the optimizations, here is a complete view of CMUs in the RMT pipeline.
SALU
SRAM
Address
Translation
Params
Processing
Set
Key
Set
Params
Initialization
Preparation
Operation
…
HASH 1
Compression
M
1
M
2
M
X
HASH 2
HASH
Composable Measurement Unit
The logical view of a CMU Group in RMT pipeline
CMU Group is a set of CMUs
share a compression stage.
deployed in parallel
Cross-stacked CMU Groups
Increase the number of deployed CMU Groups in given MAU stages (see details in the paper).
S1 | S2 | S3 | S4 | S5 | S6 | ...
 |  |  |  |  |  | ...
 |  |  |  |  |  | ...
 |  |  |  |  |  | ...
Composable Measurement Unit
Composable Measurement Unit
Cross-stacking view of CMU Groups

## Slide 24: Algorithm Implementation with CMUs
Count-min Sketch (d=3)
With CMUs, we can dynamically configure hardwares to various sketching algorithms with reconfigurable memory spaces.
  Algorithm Case#1:
    Count Min Sketch
  Algorithm Case#2:
    SuMax (Sum)
  Algorithm Case#3:
    HyperLogLog
  Algorithm Case#4:
    BloomFilter
Set parameter 2 to infinity and treat conditional addition as unconditional addition.
Cond-ADD: perform ADD operation when Param 2 larger than the value in the memory.

## Slide 25: Algorithm Implementation
SuMax (Approximate Conservative Updating, d=3)
With CMUs, we can dynamically configure hardwares to various sketching algorithms with reconfigurable memory spaces.
  Algorithm Case#1:
    Count Min Sketch
  Algorithm Case#2:
    SuMax (Sum)
  Algorithm Case#3:
    HyperLogLog
  Algorithm Case#4:
    BloomFilter
Set Param2 as the Current Minimum Counter (CMC) and ‘Cond-ADD’ will only update the counter if the counter is smaller than the CMC.

## Slide 26: Algorithm Implementation
With CMUs, we can dynamically configure hardwares to various sketching algorithms with reconfigurable memory spaces.
  Algorithm Case#1:
    Count Min Sketch
  Algorithm Case#2:
    SuMax (Sum)
  Algorithm Case#3:
    HyperLogLog
  Algorithm Case#4:
    BloomFilter
Hash()= 10 0101
Hash()= 00 0001
Hash()= 11 0101
Hash()= 01 0011
Original
HLL
FlyMon
HLL
3
2
1
1
Simulate the tracking of leading '0' with the Max operation
Equivalent to ‘0’ tracking

## Slide 27: Algorithm Implementation
With CMUs, we can dynamically configure hardwares to various sketching algorithms with reconfigurable memory spaces.
  Algorithm Case#1:
    Count Min Sketch
  Algorithm Case#2:
    SuMax (Sum)
  Algorithm Case#3:
    HyperLogLog
  Algorithm Case#4:
    BloomFilter
31/32 of the memory are wasted!

## Slide 28: Algorithm Implementation
With CMUs, we can dynamically configure hardwares to various sketching algorithms with reconfigurable memory spaces.
  Algorithm Case#1:
    Count Min Sketch
  Algorithm Case#2:
    SuMax (Sum)
  Algorithm Case#3:
    HyperLogLog
  Algorithm Case#4:
    BloomFilter
Optimized BF implementation w/
the preparation stage
Match (Param 1) | One Hot
00000… | 00…001
00001… | 00…010
... | ...
11111… | 100…000
Param Processing

## Slide 29: Implementation and Evaluation
We Implement FlyMon based on a Wedge-100BF Tofino-based programmable switch.
Runtime Rules
Data Plane
Control Plane
Grouped Deployed
(CMU Groups)
Key-selection
Phase
Attribute-oper
Phase
Address
Translation
Composable Measurement Unit (CMU)
RMT-based Hardware Switch
RMT
Implementation:
  Data Plane
    P4-16, ~5700 LOC
    9 CMU Groups (27 CMUs)
  Control Plane
    Python, ~2800 LOC
    Reconfigure built-in Algorithms
    Other essential components
  Accuracy Simulation
    C++ , ~3000 LOC
    Built-in Algorithms
Algorithm
Simulations
RMT Runtime Interfaces
Algorithm
Implementation
Resource
Management
Data
Collection
FlyMon Task Manager

## Slide 30: Implementation and Evaluation
We Implement FlyMon based on a Wedge-100BF Tofino-based programmable switch.
Runtime Rules
Grouped Deployed
(CMU Groups)
Key-selection
Phase
Attribute-oper
Phase
Address
Translation
Composable Measurement Unit (CMU)
RMT-based Hardware Switch
Data Plane
Control Plane
RMT
Implementation:
  Data Plane
    P4-16, ~5700 LOC
    9 CMU Groups (27 CMUs)
  Control Plane
    Python, ~2800 LOC
    Reconfigure built-in Algorithms
    Other essential components
  Accuracy Simulation
    C++ , ~3000 LOC
    Test built-in Algorithms
Algorithm
Simulations
RMT Runtime Interfaces
Algorithm
Implementation
Resource
Management
Data
Collection
FlyMon Task Manager

## Slide 31: Implementation and Evaluation
We Implement FlyMon based on a Wedge-100BF Tofino-based programmable switch.
Runtime Rules
Data Plane
Control Plane
RMT
RMT Runtime Interfaces
Algorithm
Implementation
Resource
Management
Data
Collection
FlyMon Task Manager
RMT-based Hardware Switch
Grouped Deployed
(CMU Groups)
Key-selection
Phase
Attribute-oper
Phase
Address
Translation
Composable Measurement Unit (CMU)
Implementation:
  Data Plane
    P4-16, ~5700 LOC
    9 CMU Groups (27 CMUs)
  Control Plane
    Python, ~2800 LOC
    Reconfigure built-in Algorithms
    Other essential components
  Accuracy Simulation
    C++ , ~3000 LOC
    Test built-in Algorithms
Algorithm
Simulations

## Slide 32: Implementation and Evaluation
We Implement FlyMon based on a Wedge-100BF Tofino-based programmable switch.
Runtime Rules
Data Plane
Control Plane
RMT-based Hardware Switch
RMT
Implementation:
  Data Plane
    P4-16, ~5700 LOC
    9 CMU Groups (27 CMUs)
  Control Plane
    Python, ~2800 LOC
    Reconfigure built-in Algorithms
    Other essential components
  Accuracy Simulation
    C++ , ~3000 LOC
    Test built-in Algorithms
Algorithm
Simulations
Key-selection
Phase
Attribute-oper
Phase
Address
Translation
Composable Measurement Unit (CMU)
Grouped Deployed
(CMU Groups)
RMT Runtime Interfaces
Algorithm
Implementation
Resource
Management
Data
Collection
FlyMon Task Manager

## Slide 33: Implementation and Evaluation
Evaluation:
  Functionality
  Resource Usage
  Accuracy (see details in the paper)
We Implement FlyMon based on a Wedge-100BF Tofino-based programmable switch.

## Slide 34: Implementation and Evaluation
Task Deployment Delay and CMU Group Usage
Millisecond-level delay: less than 100 ms.
Good expressiveness: supports at least 4 flow attributes and 10 algorithms.
Evaluation:
  Functionality
We Implement FlyMon based on a Wedge-100BF Tofino-based programmable switch.

## Slide 35: Implementation and Evaluation
Millisecond-level delay: less than 100 ms.
Good expressiveness: supports at least 4 flow attributes and 10 algorithms.
No negative impact on traffic forwarding.
Evaluation:
  Functionality
*
Impact on Traffic forwarding
We Implement FlyMon based on a Wedge-100BF Tofino-based programmable switch.

## Slide 36: Implementation and Evaluation
Evaluation:
  Functionality
  Resource Usage
Integrate CMU Groups to switch.p4
More than 3 CMU Groups can be integrated into the Tofino baseline switch project.
A CMU Group costs up to 8.334% of hardware resources (Tofino, 12 MAUs).
We Implement FlyMon based on a Wedge-100BF Tofino-based programmable switch.

## Slide 37: Implementation and Evaluation
Evaluation:
  Functionality
  Resource Usage
More than 3 CMU Groups can be integrated into the Tofino baseline switch project.
A CMU Group costs up to 8.334% of hardware resources (Tofino, 12 MAUs).
Dynamic memory: The TCAM cost of 32 memory divisions is less than 13% of one MAU Stage.
TCAM Usage of Address Translation
We Implement FlyMon based on a Wedge-100BF Tofino-based programmable switch.

## Slide 38: Implementation and Evaluation
Evaluation:
  Functionality
  Resource Usage
The number of deployable CMUs
More than 3 CMU Groups can be integrated into the Tofino baseline switch project.
A CMU Group costs up to 8.334% of hardware resources (Tofino, 12 MAUs).
Dynamic memory: The TCAM cost of 32 memory divisions is less than 13% of one MAU Stage.
Less copy: More CMU deployments.
We Implement FlyMon based on a Wedge-100BF Tofino-based programmable switch.

## Slide 39: Conclusion
Thanks!
FlyMon achieves on-the-fly reconfiguration of sketch-based measurement tasks.
  Supports on-the-fly configures measurement tasks at the millisecond level.
  Supports at least 4 common flow attributes and 10 algorithms.
  Supports dynamic memory management.
Our reference implementation of FlyMon is available at: https://github.com/NASA-NJU/FlyMon